## Slide 1: 24-783 Lecture Note 02 EX - Music Macro Language

## Slide 2: Music Macro Language
An easy way to describe a music with strings.
It used to be popular in BASIC language.
Good for earlier sound-generator chips.
Disappeared as majority of sound hardware uses PCM (Pulse Code Modulation) method, which plays back digitized sound wave, rather than synthesizing a tone.

## Slide 3: Music Macro Language
Major Advantage: You can play a music without being proficient in instruments. You at least need to be able to read music score and translate to MML.
So why was it difficult with modern system? In addition to MML parser, it requires a module for synthesizing tones.
Many computers used to have YAMAHA YM sound chip for synthesizing tones.

## Slide 4: YAMAHA YM2612 chip
YM-series is a family of YAMAHA FM Synthesizer LSIs.
FM stands for Frequency Modulation.
YM2612 was used by SEGA arcade games and game consoles.
Also used Fujitsu FMTOWNS-series computer (The last computer I pledged loyalty to!)
Cheaper version YM2203 was used in many 8-bit computers and game consoles.
YAMAHA YM2203C and 3812 chips

## Slide 5: MML Player and YAMAHA YM2612 Emulator Libraries
Git Repository.
  https://github.com/captainys/MMLPlayer.git
From CMake, add two sub-directories:
  mmlplayer
  ym2612

## Slide 6
Let's listen to what kind of music you can play with these libraries.

## Slide 7: How the Libraries Work?
MML Player library interprets MML and generates a fragment of 44.1KHz wave.
YsSimpleSound library plays the wave.
MML "O4CDEFGAB"
MML Player Library
44.1KHz Wave
YsSimpleSound library
PC Speaker

## Slide 8: Using a MML Player Library
Sub-directories in MML Player repository:
  ym2612
  mmlplayer
Two header files:
  yssimplesound.h
  mmlplayer.h

## Slide 9: Initializing Sound Player for Streaming
Once at the beginning of the program:
Create three variables:
  MMLSegmentPlayer mmlplayer;
  YsSoundPlayer player;
  YsSoundPlayer::Stream stream;
Then start player and streaming.
  player.Start();
  player.StartStreaming(stream);

## Slide 10: Set Up MML
Use mmlplayer.AddSegment function to add MML strings.
Currently mmlplayer library supports single YM2612 emulation, which has 6 channels.
Therefore AddSegment function takes six strings.

## Slide 11: General Structure of the Program
wavePiece=Generate first wave fragment
while(termination!=true)
{
player.KeepPlaying(); // For Linux ALSA library
if(Audio stream can accept the next segment)
{
Send wavePiece to the stream.
wavePiece=next wave fragment
}
}

## Slide 12: Let's Take a Look at the Moon-Light Sonata Source Code

## Slide 13: MML Tutorial
Note
#
b
O4C D E F G A B O5C O4F+ B- R
O4F#

## Slide 14: MML Tutorial
Tempo
  T120
  T60
x120 per minute
x60 per minute or x1 per second

## Slide 15: MML Tutorial
Length
# .
b
C8 D16 L8EFG L16AB O5C. O4F+. B-16 R4
.
O4F#.

## Slide 16: MML Tutorial
No Key-Off after a tone.
O4A4& A16

## Slide 17: MML Tutorial
Instrument
@1 E.PIANO
@2 PIANO
@3 TRUMPET
@4 TRUMPET
@5 HARPSICHORD
@6 ORGAN
@7 OBOE
@8 CLARINET
@9 WOODWIND
@10 GUITAR
@11 KOTO
@12 HARP
@13 E.BASE
@14 DRUM
@15 DRUM
@16 BELL
@17 BELL
@18 BELL
@19 ELECTRIC
@20 ELECTRIC
@21 ELECTRIC
@23 METALIC
@24 METALIC
@25 METALIC
@26 PSG
@27 FNYON
@28 NOISE

## Slide 18: MML Tutorial
Qn Specify how long the key needs to be ON. It is like how long a key is held down in piano. Q4 means half the length of the tone. Q8 (default) means full length. Essentially, "Q4C4" is same as "C8R8". Like other MML syntax, Qn affects all subsequent tones until next Qn is given.
Vn Volume. V0 is minimum. V15 is maximum.
> One octave up.
< One octave down.
MML player will ignore spaces.

## Slide 19: Using MML Player Library
3 Libraries:
  yssimplesound
  mmlplayer
  ym2612
yssimplesound library is in the public repository.
mmlplayer and ym2612 libraries are in the MMLPlayer repository.
By the way, include mmlplayer.h before fssimplewindow.h. Windows.h is included from fssimplewindow.h, which defines some macros that contradicts with mmlplayer.h

## Slide 20: Using MML Player Library
In your top-level CMakeLists.txt: add_subdirectory(relative-path-to-public ${CMAKE_BINARY_DIR}/public) add_subdirectory(relative-path-to-MMLPlayer/mmlplayer ${CMAKE_BINARY_DIR}/mmlplayer) add_subdirectory(relative-path-to-MMLPlayer/ym2612 ${CMAKE_BINARY_DIR}/ym2612)
In your CMakeLists.txt for executable:
  add_executable(myProgram MACOSX_BUNDLE source.cpp) target_link_libraries(myProgram fssimplewindow mmlplayer ym2612 yssimplesound_platform)

## Slide 21: Four Variables for Using MMLPlayer Library
  YsSoundPlayer soundPlayer;
  YsSoundPlayer::Stream soundStream;
  YsSoundPlayer::SoundData nextWave;
  MMLSegmentPlayer mmlPlayer;

## Slide 22: Initialization
Start Sound Player by:
  soundPlayer.Start();
Start Sound Streaming by:
  soundPlayer.StartStreaming(soundStream);
Add MML segments in mmlPlayer.

## Slide 23: Playing Music
In each step (in the main loop or RunOneStep)
soundPlayer.KeepPlaying(); // Needed for supporting Linux.
if(soundPlayer.StreamPlayerReadyToAcceptNextSegment(soundStream,nextWave))
{
soundPlayer.AddNextStreamingSegment(soundStream,nextWave);
auto rawWave=mmlPlayer.GenerateWave(100);
nextWave.CreateFromSigned16bitStereo(YM2612::WAVE_SAMPLING_RATE,rawWave);
if(0!=mmlPlayer.GetLastErrorCode())
{
for(auto msg : mmlPlayer.GetLastError().Format())
{
std::cout << msg << std::endl;
}
}
}